## Slide 1
RTL code for Digital Designs
in Verilog & VHDL
A beginner-friendly guide to describing gates, muxes, decoders, flip-flops, registers, counters, and testbenches in two hardware description languages.
Main Structure
Combinational Logic
Register
Counter
Shift-register
Mental model: HDL code describes hardware structure and behavior. Simulation runs over time; synthesis maps suitable code into gates and flip-flops.
01 Basic logic elements in Verilog & VHDL
FSM

## Slide 2
HISTORY
1947 the transistor invention
1958 the first integrated circuit
1971 Intel introduce Intel 4004 the first IC CPU. 4 bits processor made of 2300 transistors.
VHDL
1983 – US Department Of Defense (DOD) request from IBM, TI & Intermates Labs to develop a new standard language for Hardware Design Development.
VHDL = VHSIC Hardware Description Language
(VHSIC - Very High-Speed Integrated Circuit)
VITAL = VHDL Initiative Toward ASIC Libraries
1987 – VHDL IEEE-1076 Standard is released
1988 – First VHDL simulators
1990 – First VHDL projects in Israel, mainly for military companies.
1993 – VHDL IEEE-1076-93 released.
1995 Standard VITAL’95 is released for simulation of Gate-Level libraries.
VHDL 200X – The Future of VHDL. Enhance/update VHDL to improve performance, modeling capability, ease of use, simulation control, and the type system.
Verilog
1984: Gateway Design Automation introduced Verilog.
1989: Gateway merged into Cadence Design Systems.
1990: Cadence put Verilog HDL into the public domain
(OVI = Open Verilog International).
1995: IEEE standardized the Verilog IEEE 1364-1995.
2001: IEEE standardized the Verilog IEEE 1364-2001.
2002: Accellera publishes System Verilog.
Accelerate is the merged replacement of OVI & VHDL
International (VI).
2005: IEEE standardized the System Verilog IEEE 1800-2005.

## Slide 3
Main Structure
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
module Master #(
parameter WIDTH = 4
)(
input clk,
output [WIDTH :0] data,
);
wire [WIDTH -1:0] wireData;
Reg [WIDTH -1:0] regData;
endmodule
entity Master is
generic (
WIDTH : integer := 4
);
Port (
Start : in STD_LOGIC;
Data: in STD_LOGIC_VECTOR (WIDTH-1 downto 0 );
);
end Master;
architecture Behavioral of Master is
component ComponentName is
Port (
);
end component ComponentName;
signal start : std_logic;
signal data : std_logic_vector (WIDTH-1 downto 0);
begin
Logic
end Behavioral;
VHDL
Verilog

## Slide 4
Combinational Logic
VHDL
Verilog
signal start : std_logic := ‘0’/‘1’;
signal data : std_logic_vector (WIDTH-1 downto 0) := x”0000;
signal index_count : unsigned(7 downto 0) := x"00";
signal temperature : signed(11 downto 0);
1’bx; 8’h00; 0;
wire [WIDTH -1:0] wireData = {WIDTH{1’b0}};
reg [WIDTH -1:0] regData;
reg signed [WIDTH-1:0] signed_reg = {WIDTH{1'b0}};
wire a, b;
assign a = b;
assign a = !b;
assign a = ~b;
wire a, b, c;
assign a = a || b; // or
assign a = a && b; // and
assign a = a ^ b; // xor
signal a, b : std_logic;
a <= not b; // not
a <= a or b; // or
a <= a and b; // and
a <= a xor b; // xor
use ieee.numeric_std.all;
vec_out <= std_logic_vector(to_unsigned(int_in, WIDTH));
my_integer <= to_integer(unsigned(my_std_logic_vector));
vec_out <= std_logic_vector(to_signed(int_in, WIDTH));
unsigned_signal <= to_unsigned(42, my_vector'length);
signal r_buffer : std_logic_vector(vector_out'range);

## Slide 5
Combinational Logic (arrays)
VHDL
Verilog
wire [WIDTH -1:0] wireData [0:DEPTH1-1] [0:DEPTH2-1] ={DEPTH {WIDTH{1’b0}}};
assign wireData[1][3] = Data;
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
package my_types_pkg is
type matrix_1d is array (0 to 3) of std_logic_vector(7 downto 0);
type array_2d is array (0 to 1) of matrix_2d;
end package my_types_pkg;
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
library work;
use work.my_types_pkg.all;
entity top_module is
port (
);
end entity top_module;
architecture behavioral of top_module is
signal my_3d_grid : array_2d := (others =>(others =>(others =>'0')));
begin
my_3d_grid(1)(3) <= "01011010";
end architecture behavioral;

## Slide 6
Combinational Select (MUX)
Verilog
sel(0)
0
1
a
out
sel(1)
0
1
b
sel(2)
0
1
c
d
VHDL
wire a, b, c, d;
wire [2:0] sel;
wire out;
assign out = (~sel[0]) ? a :
(~sel[1]) ? b :
(~sel[2]) ? c : d;
signal a, b, c, d : std_logic;
signal sel : std_logic_vector (2 downto 0);
Signal out : std_logic;
out = a when sel(0) = ‘0’ else
b when sel(1) = ‘0’ else
c when sel(2) = ‘0’ else d;

## Slide 7
Comparator
Verilog
VHDL
wire sel;
wire [WIDTH -1:0] A,B;
assign sel = ( A == B ) ? 1'b1 : 1'b0; Equal to
assign sel = ( A === B ) ? 1'b1 : 1'b0; Strictly Equal to
assign sel = ( A != B ) ? 1'b1 : 1'b0; Not Equal to
assign sel = ( A > B ) ? 1'b1 : 1'b0; Greater than
assign sel = ( A >= B ) ? 1'b1 : 1'b0; Greater or Equal
assign sel = ( A < B ) ? 1'b1 : 1'b0; Less than
assign sel = ( A <= B ) ? 1'b1 : 1'b0; Less or Equal
signal sel : std_logic;
signal A,B : std_logic_vector (WIDTH -1 downto 0) ;
sel <= '1' when A = B else '0';
sel <= '1' when A /= B else '0';
sel <= '1' when A > B else '0';
sel <= '1' when A >= B else '0';
sel <= '1' when A < B else '0';
sel <= '1' when A <= B else '0';
A
B
‘1’
‘0’
sel

## Slide 8
Combinational Select (MUX)
Verilog
VHDL
wire a, b, c, d;
wire [1:0] sel;
wire out;
always @(*) begin
case (sel)
2'b00 : out = in0;
2'b01 : out = in1;
2'b10 : out = in2;
2'b11 : out = in3;
default : out = 1'b0;
endcase
end
signal a, b, c, d : std_logic;
signal sel : std_logic_vector (1 downto 0);
Signal out : std_logic;
mux_process : process(sel, a, b, c, d)
begin
case sel is
when "00" => out<= in0;
when "01" => out<= in1;
when "10" => out<= in2;
when "11" => out<= in3;
when others => out<= '0’;
endcase;
end process mux_process;
sel
2’b00
2’b01
2’b10
2’b11
a
b
c
d
out

## Slide 9
Registers
D
Q
D
Q
in
out
clk
A
B
reset
Tco​+Tdata​ ​≤ Tclk -Tsetup ​​
Tco
Tdata
in
A
B

## Slide 10
Shift Register
D
Q
D
Q
in
clk
A
B
reset
D
Q
D
Q
out
C
D
in0
in1
in0
in1
in0
in2

## Slide 11
Shift Register
Verilog
VHDL
wire clk,
wire rst_n,
wire shift_en,
wire serial_in,
reg [WIDTH-1:0] data_out
always @(posedge clk or negedge rst_n)
if (!rst_n) data_out <= {WIDTH{1'b0}};
else if (shift_en) data_out <= {data_out[WIDTH-2:0], serial_in};
signal clk : std_logic;
signal rst_n : std_logic;
signal shift_en : std_logic;
signal serial_in : std_logic;
signal data_out : std_logic_vector(WIDTH-1 downto 0);
signal r_shift : std_logic_vector(WIDTH-1 downto 0);
shift_process : process(clk, rst_n)
begin
if rst_n = '0' then
r_shift <= (others => '0'); -- Clear all register stages
elsif rising_edge(clk) then
if shift_en = '1' then
r_shift <= r_shift(WIDTH-2 downto 0) & serial_in ;
end if;
end if;
end process shift_process;
data_out <= r_shift;
Reg [7:0] counter
rstn
clk
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
in1

## Slide 12
counter
Verilog
VHDL
wire clk,
wire rstn,
wire count_en,
reg [WIDTH-1:0] count,
always @(posedge clk or negedge rstn)
if (!rstn) count <= {WIDTH{1'b0}};
else if (count_en) count <= count + 1'b1;
signal clk : std_logic;
signal rst_n : std_logic;
signal count_en : std_logic;
signal count : out std_logic_vector(WIDTH-1 downto 0);
signal r_count : unsigned(WIDTH-1 downto 0);
count_process : process(clk, rst_n)
begin
if rst_n = '0' then
r_count <= (others => '0');
elsif rising_edge(clk) then
if count_en = '1' then
r_count <= r_count + 1;
end if;
end if;
end process count_process;
count <= std_logic_vector(r_count);
Reg [7:0] counter
rstn
clk
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 2 | 2
1 | 1 | 0 | 0 | 3 | 3
0 | 0 | 1 | 0 | 4 | 4
1 | 0 | 1 | 0 | 5 | 5
0 | 1 | 1 | 0 | 6 | 6
1 | 1 | 1 | 0 | 7 | 7
0 | 0 | 0 | 1 | 8 | 8
1 | 0 | 0 | 1 | 9 | 9
0 | 1 | 0 | 1 | A | 10
1 | 1 | 0 | 1 | B | 11
0 | 0 | 1 | 1 | C | 12
1 | 0 | 1 | 1 | D | 13
0 | 1 | 1 | 1 | E | 14
1 | 1 | 1 | 1 | F | 15
use ieee.numeric_std.all;
use ieee.std_logic_unsigned.all

## Slide 13
Registers
Verilog
VHDL
wire clk,
wire rstn,
wire en,
wire [WIDTH -1:0] data_in,
reg [WIDTH -1:0] data_out
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
data_out <= {WIDTH{1’b0}}
end else if (en) begin
data_out <= data_in;
end
end
always @(posedge clk or negedge rstn)
if (!rstn) data_out <= {WIDTH{1’b0}};
else if (en) data_out <= data_in;
signal clk : std_logic;
signal rst_n : std_logic;
signal en : std_logic;
signal data_in : std_logic_vector(WIDTH-1 downto 0);
signal data_out : std_logic_vector(WIDTH-1 downto 0);
reg_process : process(clk, rst_n)
begin
if rst_n = '0' then
data_out <= (others => '0');
elsif rising_edge(clk) then
if en = '1' then
data_out <= data_in;
end if;
end if;
end process reg_process;
Reg [7:0] register
DataOut
Data In
en
rstn
clk

## Slide 14
Hierarchical design (child)
Verilog
VHDL
module bus_converter_child #(
parameter IN_WIDTH = 16, // Default input size
parameter OUT_WIDTH = 8 // Default output size
)(
input [IN_WIDTH-1:0] raw_data_in,
output [OUT_WIDTH-1:0] reduced_data_out
);
// Simple truncation: takes the lowest 'OUT_WIDTH' bits from the input
assign reduced_data_out = raw_data_in[OUT_WIDTH-1:0];
endmodule
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity bus_converter_child is
generic (
IN_WIDTH : integer := 16; -- Default input size
OUT_WIDTH : integer := 8 -- Default output size
);
port (
raw_data_in : in std_logic_vector(IN_WIDTH-1 downto 0);
reduced_data_out : out std_logic_vector(OUT_WIDTH-1 downto 0)
);
end entity bus_converter_child;
architecture behavioral of bus_converter_child is
begin
-- Slice the input vector from index (OUT_WIDTH-1) down to 0
reduced_data_out <= raw_data_in(OUT_WIDTH-1 downto 0);
end architecture behavioral;

## Slide 15
Hierarchical design (parent)
Verilog
VHDL
module system_top (
// Audio path signals
input [31:0] audio_32bit_in,
output [15:0] audio_16bit_out
);
// Instance 1: Converts 32-bit audio down to 16-bit
bus_converter_child #(
.IN_WIDTH(32),
.OUT_WIDTH(16)
) audio_dsp (
.raw_data_in(audio_32bit_in),
.reduced_data_out(audio_16bit_out)
);
endmodule
library IEEE;
use IEEE.STD_LOGIC_1164.all;
entity system_top is
port (
-- Audio path signals
audio_32bit_in : in std_logic_vector(31 downto 0);
audio_16bit_out : out std_logic_vector(15 downto 0)
);
end entity system_top;
architecture structural of system_top is
begin
-- Instance 1: Converts 32-bit audio down to 16-bit
audio_dsp: entity work.bus_converter_child
generic map (
IN_WIDTH => 32,
OUT_WIDTH => 16
)
port map (
raw_data_in => audio_32bit_in,
reduced_data_out => audio_16bit_out
);
end architecture structural;

## Slide 16
A Final State Machine (FSM)
2’b00
2’b01
2’b10
2’b11
Start
0
1
2’b01
rstn
clk
2’b00
2’b00
2’b00
2’b10
Ready
2’b10

## Slide 17
A Final State Machine (FSM)
2’b00
2’b01
2’b10
2’b11
Start
0
1
2’b01
rstn
clk
2’b00
2’b00
2’b00
2’b10
Ready
2’b10
Verilog
module fsm_moore (
input wire clk, // System clock
input wire rst_n, // Asynchronous reset, active low
input wire start, // Input condition to start
output reg ready // Output flag (high only in STATE_B)
);
// Localparams to define state encoding (One-Hot or Binary)
localparam STATE_IDLE = 2'b00;
localparam STATE_A = 2'b01;
localparam STATE_B = 2'b10;
reg [1:0] current_state;
reg [1:0] next_state;
// 1. Sequential Block: State Register Update
always @(posedge clk or negedge rst_n) begin
if (!rst_n) begin
current_state <= STATE_IDLE;
end else begin
current_state <= next_state;
end
end
// 2. Combinational Block: Next-State Logic & Output Decoding
always @(*) begin
// Default assignments to prevent unintended latches
next_state = current_state;
ready = 1'b0;
case (current_state)
STATE_IDLE: begin
if (start) begin
next_state = STATE_A;
end
end
STATE_A: begin
next_state = STATE_B; // Unconditional transition
end
STATE_B: begin
ready = 1'b1; // Assert output in this state (Moore)
next_state = STATE_IDLE;
end
default: begin
next_state = STATE_IDLE;
end
endcase
end
endmodule

## Slide 18
A Final State Machine (FSM)
2’b00
2’b01
2’b10
2’b11
Start
0
1
2’b01
rstn
clk
2’b00
2’b00
2’b00
2’b10
Ready
2’b10
VHDL
library ieee;
use ieee.std_logic_1164.all;
entity fsm_moore is
port (
clk : in std_logic; -- System clock
rst_n : in std_logic; -- Asynchronous reset, active low
start : in std_logic; -- Input condition to start
ready : out std_logic -- Output flag (high only in STATE_B)
);
end entity fsm_moore;
architecture rtl of fsm_moore is
-- Define an enumerated type for the FSM states
type state_type is (STATE_IDLE, STATE_A, STATE_B);
signal current_state, next_state : state_type;
begin
-- 1. Sequential Process: State Register Update
state_reg_process : process(clk, rst_n)
begin
if rst_n = '0' then
current_state <= STATE_IDLE;
elsif rising_edge(clk) then
current_state <= next_state;
end if;
end process state_reg_process;
-- 2. Combinational Process: Next-State & Output Logic
comb_process : process(current_state, start)
begin
-- Default assignments to prevent latch generation
next_state <= current_state;
ready <= '0';
case current_state is
when STATE_IDLE =>
if start = '1' then
next_state <= STATE_A;
end if;
when STATE_A =>
next_state <= STATE_B; -- Unconditional transition
when STATE_B =>
ready <= '1'; -- Assert output in this state
next_state <= STATE_IDLE;
when others =>
next_state <= STATE_IDLE;
end case;
end process comb_process;
end architecture rtl;